## Slide 1: Real-time lane instance segmentation
presented by Gad Mohamed. UG computer engineering student, Nile university

## Slide 2: CONTENTS
Introduction
Literature review
Methodology
Results
Conclusion & future work

## Slide 3: Problem statement
Lane detection is a perception task in modern/autonomous vehicles that is critical in many modern cars features nowadays.
Lane keeping assistant LKA
Road edge detection

## Slide 4: Problem statement
In general, vehicle-based software solutions are complex because:
1- Limited resources on vehicle-based systems.
2- High standards imposed by safety regulations

## Slide 5: Problem statement
Particularly, lane detection is a challenging task because:
1- Variations and distortions in environment
2- Unique shape of lanes

## Slide 6: Literature review
Traditional method used feature engineering to rely on lane’s characteristics to detect them
1
2

## Slide 7: Literature review
More advanced approaches use deep-learning to improve feature extraction and robustness against environment distortions

## Slide 8: Literature review
State-of-the-art lane detection algorithms are deep-learning based !
Tested on tuSimple benchmark. Taken from: https://paperswithcode.com/sota/lane-detection-on-tusimple

## Slide 9: Methodology
Overview

## Slide 10: Methodology
Input size: 256,512,3
Output size: 256,512,2
Input image
tuSimple labels
SegNet labels
Pre-processing data
Architecture & training
Training dataset: 3626
Optimizer: Adam
Batch size: 8
Learning rate: 4e-4

## Slide 11: Methodology
Ex. 1
Ex. 2
Ex. 3
Should we use SoftMax to extract lane channel?
Post-processing data

## Slide 12: Methodology
Separating lanes
Image processing techniques like erosion and blurring are applied to separate the top point where all lanes meet in one point.

## Slide 13: Methodology
Sliding window
Sliding window 1 scans from bottom to top.
When a cluster is found, sliding window 2 scans the targeted lane starting from its seed cluster and removes it from the image.

## Slide 14: Methodology
Fitting lane
Each lane is fitted in a 3rd order function because:
  control algorithms use perception results.
  across frames, function parameters change can be expected/inferred.

## Slide 15: Results

## Slide 16: Evaluation
Work | Acc | FP | FN
SCNN | 96.53% | 0.062 | 0.0180
LaneNet(+H-net) | 96.38% | 0.078 | 0.0244
PointLaneNet(MoblieNet) | 96.34% | 0.046 | 0.0518
ENet-SAD | 96.64% | 0.060 | 0.0205
KeyPointsEstimation(32x16) | 95.75% | 0.027 | 0.0362
KeyPointsEstimation(64x32) | 96.62% | 0.031 | 0.0272
Our method | 91.83% | 0.103 | 0.096
Model | Parameters (M)
SCNN | 20.72
LaneNet(+H-net) | 15.98
PointLaneNet(MoblieNet) | 5.33
ENet-SAD | 0.98
KeyPointsEstimation(32x16) | 4.4
KeyPointsEstimation(64x32) | 4.39
Our Model | 21.67
 | LaneNet [11] | Our method
Forward pass time (ms) | 13.6 | 10
Postprocessing time (ms) | 1352 | 56
Total time (ms) | 1365.6 | 66
FPS | 0.7 | 15
Comparing our method’s speed against LaneNet
Comparing our method’s accuracy against state-of-the-art algorithms
Comparing our model parameters against state-of-the-art algorithms

## Slide 17: Conclusion & Future work
A real-time method for lane instance segmentation is proposed which runs at 15 fps on Tesla K80 GPU and achieve competitive accuracy on tuSimple benchmark.
An achievement of this work is to integrate the use of powerful deep-learning architectures and techniques with inexpensive postprocessing address both accuracy and speed challenges.
As a future work, SegNet performance will be improved by providing more data to train on and new methods will be explored to address weak points in this method namely, improving lanes separation, to increase accuracy.

## Slide 18: THANK YOU